DIGITAL PANEL METERS VNE 2

Electrical measurements 2000 points

VNE2 panel meters are well designed for industrial areas: hard housing, connection through a removable screwing connector, high immunity to external noises, several types of power supply Ac current measurement can be performed using an external transformer insuring a good insulation to the instrument in regards to line potentials.

- Dimensions : 72 x 24 mm

- Internal power supply transformer

- LED Display, 14 mm LED

Functions

(1) In ± (% of reading + number of units) at 23 ± 1°C for 1 year.

Main characteristics

Display……………………………..

2000 measurement points (3 ½ digits),

Red LED (green or yellow in option), height: 14 mm.

Overload indication by extinction of the 3 last digits.

Automatic polarity and zero……

Measurement rate………………..

2.5 measurements per second

Temperature coefficient………...

≤ accuracy / 10°C

Common mode rejection……….

≥ 110 dB at 50 Hz

Serial mode rejection……………

≥ 60 dB at 50 Hz

Current transformer……………

Suitable transformer is supplied with I 33, I 34 and I 35 models.

Primary 2 A, 20 A or 200 A.

Secondary 1 A.

200 mV on 0.2 Ω shunt.

Accuracy class 0.5 for 1 VA power.

Frequency 50 / 60 Hz.

Primary connection by plugs for 2A and 20 A ranges and metal cable gland (∅<12mm) for 200 A range.

Operating conditions……………

Nominal field of use : 0 to + 50 °C

Limit field of use : -10 to + 50°C

Power supply……………………..

230 V~ (± 10 %) 50 to 60 Hz

Other power supplies:

6 V- ± 20 % non-insulated,

5 V- ± 10 % insulated,

9 to 18 V- insulated,

18 to 36 V- insulated,

36 to 72 V- insulated,

24 V~ ± 10 % insulated,

48 V~ ± 10 % insulated,

115 V~ ± 10 % insulated.

Consumption……………………

4 VA max

Presentation………………………

ABS Case.

Sealing IP 40

Weight : around 300 g.

Connections………………………

Removable screwing connector

Options

Backlight display setting

External decimal dot commutation

command (for V- models).

Non insulated analog output

For process models D50 and D51.

1mV/digit. Acceptable load ≥ 2 kΩ.

Waterproof metal box

IP 65 Front panel

Dimensions : 99 x 36 x 120 mm

Accessories

Mechanic adaptator…..

Allows adaptation of VNE into slightly larger cutout

Adaptation of 75x25mm panel meters

External dimensions 80x32mm

Dimensions

Case    A  B  C  D Panel cut

72 x 24  72  24 5 103 68 × 22.2+

Instructions to order