FCC-1 Tuned Dipole Antenna Data

More Information

- Typical Antenna Factor Plot - 3m

Innovation, Quality, and Performance

- Typical Antenna Factor Plot - 10m

Innovation, Quality, and Performance

- Typical VSWR

Innovation, Quality, and Performance

- Numeric Data

FCC-1 Tuned Dipole Antenna Data

3 Meter | 10 Meter
Antenna Page | VSWR Graph | AF Graph

| 3 Meter Antenna Factor |
| --- |
| Frequency (MHz) | Element Length (L/2-in.) | Antenna Factor (dB/m) | Gain (dBi) |
| 25 | 96 | 2.4 | -4.2 |
| 30 | 96 | -0.7 | 0.5 |
| 35 | 82 | 0.3 | 0.9 |
| 40 | 71 1/2 | 1.2 | 1.1 |
| 45 | 63 3/4 | 2.6 | 0.7 |
| 50 | 57 | 3.5 | 0.7 |
| 55 | 54 1/2 | 4.1 | 0.9 |
| 60 | 47 1/4 | 4.6 | 1.2 |
| 65 | 45 | 4.4 | 2.1 |
| 70 | 41 | 5.5 | 1.6 |