SAS-530 Tuned Dipole Antenna Data可调偶极子天线数据

More Information

- Typical Antenna Factor Plot

Innovation, Quality, and Performance

- Typical VSWR

Innovation, Quality, and Performance

- Numeric Data

SAS-530 Tuned Dipole Antenna Data

1 Meter | 3 Meter | 10 Meter

Antenna Page | VSWR Graph | AF Graph

| 1 Meter Antenna Factor |
| --- |
| Frequency (MHz) | AF (dB/m) | Gain (dBi) | Gain (Numeric) |
| 160 | 17.2 | -2.9 | 0.52 |
| 170 | 16.9 | -2.0 | 0.62 |
| 180 | 16.9 | -1.5 | 0.70 |
| 190 | 17.3 | -1.5 | 0.71 |
| 200 | 17.2 | -0.9 | 0.81 |
| 210 | 17.5 | -0.8 | 0.83 |
| 220 | 17.8 | -0.7 | 0.85 |
| 230 | 18.2 | -0.7 | 0.85 |
| 240 | 18.3 | -0.4 | 0.90 |
| 250 | 18.4 | -0.2 | 0.96 |
| 260 | 18.2 | 0.3 | 1.08 |
| 270 | 18.3 | 0.6 | 1.14 |
| 280 | 18.3 | 0.9 | 1.23 |
| 290 | 18.1 | 1.4 | 1.38 |
| 300 | 18.5 | 1.3 | 1.35 |
| 310 | 18.3 | 1.8 | 1.50 |
| 320 | 18.5 | 1.8 | 1.53 |
| 330 | 18.7 | 1.9 | 1.55 |
| 340 | 19.0 | 1.9 | 1.54 |
| 350 | 19.5 | 1.6 | 1.45 |
| 360 | 19.8 | 1.6 | 1.44 |
| 370 | 20.7 | 0.9 | 1.23 |
| 380 | 20.8 | 1.0 | 1.27 |
| 390 | 21.5 | 0.6 | 1.14 |
| 400 | 21.9 | 0.4 | 1.09 |
| 410 | 21.9 | 0.6 | 1.15 |
| 420 | 22.2 | 0.5 | 1.13 |
| 430 | 22.2 | 0.7 | 1.18 |
| 440 | 22.7 | 0.4 | 1.10 |
| 450 | 23.1 | 0.2 | 1.05 |
| 460 | 23.4 | 0.1 | 1.02 |
| 470 | 24.2 | -0.5 | 0.89 |
| 480 | 24.1 | -0.2 | 0.95 |
| 490 | 24.7 | -0.6 | 0.86 |
| 500 | 25.0 | -0.8 | 0.84 |

| 3 Meter Antenna Factor |
| --- |
| Frequency (MHz) | AF (dB/m) | Gain (dBi) | Gain (Numeric) |
| 160 | 16.6 | -2.3 | 0.59 |
| 170 | 16.3 | -1.4 | 0.72 |
| 180 | 16.2 | -0.8 | 0.82 |
| 190 | 16.2 | -0.4 | 0.92 |
| 200 | 16.2 | 0.1 | 1.02 |
| 210 | 16.1 | 0.6 | 1.15 |
| 220 | 15.9 | 1.2 | 1.32 |
| 230 | 15.9 | 1.6 | 1.44 |
| 240 | 16.3 | 1.6 | 1.43 |
| 250 | 16.4 | 1.8 | 1.52 |
| 260 | 16.8 | 1.7 | 1.49 |
| 270 | 17.2 | 1.7 | 1.47 |
| 280 | 17.6 | 1.6 | 1.44 |
| 290 | 17.8 | 1.7 | 1.48 |
| 300 | 18.1 | 1.7 | 1.48 |
| 310 | 18.4 | 1.7 | 1.47 |
| 320 | 18.6 | 1.7 | 1.50 |
| 330 | 19.0 | 1.6 | 1.45 |
| 340 | 19.3 | 1.6 | 1.44 |
| 350 | 19.4 | 1.7 | 1.49 |
| 360 | 19.7 | 1.7 | 1.47 |
| 370 | 20.1 | 1.5 | 1.42 |
| 380 | 20.5 | 1.3 | 1.36 |
| 390 | 20.9 | 1.2 | 1.31 |
| 400 | 21.2 | 1.1 | 1.28 |
| 410 | 21.4 | 1.1 | 1.29 |
| 420 | 21.7 | 1.0 | 1.26 |
| 430 | 21.3 | 1.6 | 1.45 |
| 440 | 21.9 | 1.2 | 1.32 |
| 450 | 21.8 | 1.5 | 1.42 |
| 460 | 22.1 | 1.4 | 1.38 |
| 470 | 22.6 | 1.1 | 1.28 |
| 480 | 22.6 | 1.3 | 1.34 |
| 490 | 22.7 | 1.4 | 1.36 |
| 500 | 22.8 | 1.4 | 1.39 |

| 10 Meter Antenna Factor |
| --- |
| Frequency (MHz) | AF (dB/m) | Gain (dBi) | Gain (Numeric) |
| 160 | 16.3 | -2.0 | 0.64 |
| 170 | 15.8 | -0.9 | 0.80 |
| 180 | 16.0 | -0.6 | 0.86 |
| 190 | 16.5 | -0.7 | 0.86 |
| 200 | 15.9 | 0.4 | 1.09 |
| 210 | 16.4 | 0.3 | 1.07 |
| 220 | 16.0 | 1.1 | 1.29 |
| 230 | 16.1 | 1.4 | 1.37 |
| 240 | 16.4 | 1.5 | 1.40 |
| 250 | 16.3 | 1.9 | 1.55 |
| 260 | 17.0 | 1.5 | 1.43 |
| 270 | 16.7 | 2.2 | 1.65 |
| 280 | 17.2 | 2.0 | 1.58 |
| 290 | 17.1 | 2.4 | 1.74 |
| 300 | 17.8 | 2.0 | 1.58 |
| 310 | 17.8 | 2.3 | 1.69 |
| 320 | 18.3 | 2.0 | 1.60 |
| 330 | 18.4 | 2.2 | 1.67 |
| 340 | 19.1 | 1.8 | 1.51 |
| 350 | 19.0 | 2.1 | 1.63 |
| 360 | 19.7 | 1.7 | 1.47 |
| 370 | 20.0 | 1.6 | 1.45 |
| 380 | 20.3 | 1.5 | 1.43 |
| 390 | 21.1 | 1.0 | 1.25 |
| 400 | 20.3 | 2.0 | 1.58 |
| 410 | 21.3 | 1.2 | 1.32 |
| 420 | 20.5 | 2.2 | 1.66 |
| 430 | 21.1 | 1.8 | 1.52 |
| 440 | 21.7 | 1.4 | 1.39 |
| 450 | 21.4 | 1.9 | 1.55 |
| 460 | 22.3 | 1.2 | 1.32 |
| 470 | 22.6 | 1.1 | 1.28 |
| 480 | 22.8 | 1.1 | 1.28 |
| 490 | 23.2 | 0.9 | 1.22 |
| 500 | 23.3 | 0.9 | 1.24 |

- Cross Polarization Attenuation